## Slide 1: Artemmis Training – The Simple HMI Business Unit ID
Revision: 1.0

## Slide 2: The Simple HMI Definition
Simple HMI world:
  Represents the static scenes
    Widget
    Widget tree structure
    Widget visual representation
  Applies simple drawing concept
    Draws with 1 task and surface
    Basic window tree concept
    Painter’s algorithm to consider
  Supports data binding to modeller (application)
  Includes the required behaviors
    Widget communication (user interaction, inter-widget links)
    Scene management

## Slide 3
Static Scene
Representation

## Slide 4: The Simple HMI Sample display requirements
85 %
Image change to sad face when value < 20, and smiley when value > 70. In all other case, It’s not showing.
Text displays the numeric value of the bar above.
Center aligned in the middle of the display.
Font : Calibri 30
Color: Red
Green bar shows the current oil level in the range of 0-100.
Bar size: 200 x 40 pixels (centered)
Display size: 240 x 320

## Slide 5: Widget Concept
Definition:
  A widget (window gadget) is an element of a Graphical User Interface (GUI) that displays an information arrangement changeable by the user
Characteristics:
  has a set of properties that can be linked to a model
  has a view part that draws the widgets
  has a controller part that defines the behavior of the widget
  reacts on user interaction
  follows an object oriented approach
  can be arranged hierarchical
Widget
Properties
View
Controller
Model

## Slide 6: Widget States (1)
The following are the various states of the widgets:
  New: Newly constructed widget.
  Init: Widget has received Tree Init notification and is going through initialization for the first time.
  Running: Widget has been initialized. At the end of tree build/change it will receive Tree Build Done notification.
  Changing Trees: Widget has been detached from old tree and being moved to new tree.
  Prepare To Destroy: Widget is being destroyed as it is not present in the new scene.
  Init Again: Widget has been attached to a new tree and has received Tree Init notification.
  Running Again: Widget is back to stable in a new tree.

## Slide 7: Widget States (2)

## Slide 8: Widget States (3)
IsStateNew = false boIsReadyForClientAccess = false
Widget Builder
Construction
Properties initialized
Pre Hook
State change
Property propagation
Final Hook
API values copied
Message Hooks
Time
State change (instant, no message)
New
Init
Running
TreeInit message
TreeBuildDone message
IsStateNew = true boIsReadyForClientAccess = false
Tree is fully built
State is changed
to Running instantly (no message)
for entire subtree
IsStateNew = false boIsReadyForClientAccess = true

## Slide 9: Widget Base Properties
Widget base class defines the base properties which are inherited by all widgets. The initial values of these properties are configured in the model.
  Focus This property determines the path of focused message in widget tree.
  Focusable This property determines whether a widget instance is allowed to be set to Focused.
  Visibility This property determines whether or not a widget should be drawn on the display.
  Enabled This property is another property of widget instances, although it doesn’t have any effect internally, it is available for use by clients.
  Do Update This property determines whether or not an instance is allowed to receive API updates.
Each widget has its own property, but the actual effect is taking place when the cummulative value from root until the widget are all true. For example: we have this constellation => root (visible) – A (invisible) – B (visible) In the actual display: A and B are both not visible!

## Slide 10: Example – Widget Properties
Not Focused, Enable, Visible,
Focused, Enable, Visible,
Not Focused, Disable, Visible,
Not Focused, Disable, InVisible,

## Slide 11: Widget Classes, Widget Objects & Widget Tree
Memory Representation: Widget Object Tree
Visual Representation
Title
Section
A
Clock
ScrollBar
Section
B
Scene
#1
Date
Country
Lang
Back
ListBox
Frame
Title
Clock
Date
Language
Country
Back
Widget Classes
TextArea
ListBox
Button
Frame
ScrollBar
Widget Objects

## Slide 12: Widget Base Classes
The framework provided a basic set of widgets in WFC package
  WidgetExtension: empty implementation where project can add own attributes
  Controller widget type: has a link to state machine / controller strategy
  SLCDElement: base class for SLCD widget (special paint for SLCD module)
  Warning widget: special widget to be used with WWS package
Sample widgets: Image, StaticText, Text, ListBox, Button, ToggleButton – not in official delivery

## Slide 13: Workflow – Custom Widget implementation (1)
Design
  Think about:
    Properties (data, logical, visual)
    Class Inheritance/Hierarchy
    Behavior
      Class-level
      Instance-level (via generated final hooks)
    Re-use possibilities
  Also consider: maybe a Scene Manager + StateMachine + primitive widgets (images, texts) are sufficient!

## Slide 14: Workflow – Custom Widget implementation (2)
Implementation
  Create an XML Type Description for your WidgetType
  Implement the C++ code:
    All your XML-declared property setters
    WCS::enStatusMessage enProcessMessage(Message *m)
      Check the message ID, type and (optionally) data, implementing functionality if necessary, like:
        Change properties, fire events, etc.
        Invalidate if necessary, to cause a repaint
      Return the correct status (eg, CONSUME to remove the message)
    void vDraw( uint16 u16GRLCContext )
      Call GRLC functions to render your widget state
      Note: Coordinates provided to GRLC calls (eg GRLC_vDrawBitmapAt( x, y )) are relative to the widget’s position (relative to top left widget corner)

## Slide 15
Simple Drawing Concept

## Slide 16: Widget Visualization (1)
A Widget object covers a rectangular area on the display (that is widget window), which is determined by its x- and y-position and by its x- and y-dimension (size and height).
A Widget Tree consists out of Widgets in parent-child relationship
A child widget is always visually contained inside a parent widget. It may never exceed the bounding box of its parent (Containment relationship), and the position values are relative to parent window.
Widgets are allowed to overlap on the display
If two widgets have an overlapping area, the z-position of the widget determines, which of both will be rendered in the front and which will be rendered behind the other widget
Widget z-positions is implicitly defined or can be set explicitly
If the z-position of a widget is not explicitly set, its z-position is determined by its position within the widget tree (implicit z-positioning) by the use of a depth-search algorithm
The rendering sequence of multiple widgets is executed from lowest z-order to the highest z-order (shown in red numbers)
Title
Section
A
Clock
ScrollBar
Section
B
Scene
#1
Date
Country
Lang
Back
ListBox
Lowest z-order
 „Back“
Highest z-order
 „Front“
1
3
2
5
4
6
7
9
8
10
11
Rendering Sequence

## Slide 17: Widget Visualization (2)
CIA controls the painting on the display. Therefore, the base widget class derives from CIA::Painters.
When CIA orders its painter (widget) to paint, a drawing function of widget will be called.
Widget’s method vDraw is is the place to specify the widget’s visual representation by calling relevant GRLC methods.
Some rules:
  Always call Widget base class vDraw method at the beginning of derived widget’s vDraw. It will perform the clearing of widget’s window area before redrawing the content.
  Pass on the drawing properties (composition mode, font, alignment, etc) as necessary to relevant GRLC function calls during draw.
  Drawing position to be passed to GRLC is relevant to the widget window’s position / size and is dependent on alignment.
  Drawing context attribute is reset by framework before painting each widget. Don’t assume the previously set context Is still valid!
17 / T. A. Devi / ID RD CDS HF / Dec-2012 © Continental Automotive Singapore

## Slide 18: Image Assembly
Widget Tree
Widget
Window
contains the view of one or more widgets
can be stacked in z-order (overlapping)
is used to decompose a scene
is painting on a surface
is not buffered
accesses the surface to draw its contents via a BUFlet
can be transparent (true/false), but has no alpha-channel
Srfc
Buffer
Srfc
Buffer
Srfc
Buffer
BUFlet
-manages the buffers of a surface
-handles the flip operation
-hides the buffer management to the windows
-optimizes the drawing operations on surface level
-handles drawing contexts
Widget
BUFlet
Surface
has a relation to a buffer (off-screen or layer)
has an alpha channel
can be stacked in z-order (overlapping)
is visible or invisible
Notes: Flip handling of surface is done by framework => for multiple buffer surfaces
Only layer will be shown on display

## Slide 19: Drawing Contents to Surface
Painter
Widget
BUFlet
Window
Surface
Paint
Event
Attach BUFLet
Call Painter
Paint into
Buffer
Painter
base class implementing the paint method
paints its contents into a surface buffer resource
BUFlet
executes the flipping of buffers
Detach BUFLet
WMapp
Window
receives the paint event
attaches the buflet for painting
broadcasts the paint to its children
requests a painter (e.g. Widget) for painting
detaches the buflet

## Slide 20: System Integration Task model and execution
CIA_TimeDomainHMI
Task
prio
high
low
…
…
CIA_Manager
CSHDL_InitDeinit
CompositeManager
HMI Msg-Processing
Paint of HMI content
IDLE
CIA_TimeDomainHMI
EPF
CIA
Paint
Process Msg‘s
All CIA related task‘s have to be extended and full preemptive (using Semaphores)
CIA_Manager
Filp (sync.)
Notes: You have to configure in AROS the TimeDomain_HMI and to configure the CIA event usage in that task within the CIA.sdh configuration file.
The CIA – Manager can be used in an exisiting event driven context

## Slide 21: Painter’s Algorithm
How would a painter draw this scene?
21 / T. A. Devi / ID RD CDS HF / Dec-2012 © Continental Automotive Singapore
How would the window tree look like?

## Slide 22: Painter’s Algorithm
Paint the sky
Paint the sun
Paint the cloud
Paint the ground
Paint the tree
22 / T. A. Devi / ID RD CDS HF / Dec-2012 © Continental Automotive Singapore
Sun
Section
A
Tree
Section
B
Widget tree
root
Ground
Sky
Cloud
Clear
Root
Buflet
(surface)
Window tree:
Widget window tree
Generally, for widget painter, window tree is equal to widget tree. Widget window is also implicitly managed by the widget.

## Slide 23: Demo 1 Sample display requirements (revisit)
85 %
Image change to sad face when value < 20, and smiley when value > 70. In all other case, It’s not showing.
Text displays the numeric value of the bar above.
Center aligned in the middle of the display.
Font : Calibri 30
Color: Red
Green bar shows the current oil level in the range of 0-100.
Bar size: 200 x 40 pixels (centered)
Display size: 240 x 320
Ignore this part for now!
- For first static scene,
hard-coded value 85% is used
- Default state for Smiley SM is
happy

## Slide 24: Demo 1 Display decomposition
85 %
Break down the scene into smallest possible entities (i.e. widgets)
Identify if we need special type of widget
  Do we need extra attribute?
  Do we need special behavior support?
Create the widget tree structure
  Consider painter’s algorithm
(1) Special widget: SimpleGauge
(2) Text widget (dynamic and RSST ID)
(3) Visibility controller + 2 image widgets
Widget and window tree:
Text
Happy
Visibility
Controller
Scene
#1
Sad
Simple
Gauge
Widget tree
root
Clear
Root
Buflet
(surface)

## Slide 25: Demo 1 Creating Custom Widget: SimpleGauge
Set MinValue=0, MaxValue=100 (assumed to be not changeable)
CurValue initial value to be defined in model
FgColor and BgColor can be changed via model. Default: as above.
Use the GRLC_vPrimSetDrawColor & GRLC_vFillRect methods
Implement C++ class to realize the widget
MaxValue
MinValue
CurValue
FgColor
BgColor

## Slide 26: Demo 1 Bridging model world and code
Brutus only understands HMI XML language
  Need to translate widget classes (C++ code) to XML (i.e. type descriptor)
  Type descriptor must be added for new derived widgets / WMApps only
  Only properties and methods listed in type descriptors can be used in model
TD folder => collection of type descriptors
Type descriptor:
  Specify declaration file (the actual C++ header file)
  Specify the properties which are accessible from model
  Specify setters and getters (if necessary)
  Specify the init / default values of those properties
  Specify constructor and its string of parameter
  Specify methods which are callable from model

## Slide 27: Demo 1 Graphical Resources Preparation
RSSTExport tool
  Create / modify grADI_Project.xml and RSST_Export.xml
  Usually the 2 files work as a pair with grADI focuses on specifying input files or model related values and RSST focuses on the output or target configuration.
  Important tags to look out for:
    Language, PixmapResource, PixFontResource, StringResource, ColorFormat/PixFormat, Dependency, SurfaceDescriptor, TargetConfiguration
ROMG tool
  Create / modify Cache.xml
  Important section: ApplicationCache
  Surfaces => memory linked to SurfaceDescriptor configuration in RSST
    Cardinality = #buffers, memory size = width*height*pixel depth
  Texts and TmpTexts => memory for text decompression
Notes: For more detailed training of both tools, contact the Graphics group

## Slide 28: Demo 1 Modelling the widget tree
Widgets folder => to add widget tree model
  Define the widget structure according to the tree we have designed
  Each file can represent a single widget or a subtree
  “FileLink” is used to link the subtree within 1 XML to another widget (sibling / child)
  Specify the object specific properties => overwrite the default from TD
    Example: width, height, position, focused, visible, etc.
Text
Happy
Visibility
Controller
Scene
#1
Sad
Simple
Gauge
Widget tree
root
Clear
Root
Buflet
(surface)
Widget tree structure
Individual widget objects
SM
Just config basic default state for now

## Slide 29: Demo 1 Modelling the drawing task and image assemblies (1)
CIA folder => to configure drawing task (time domain) and assemblies (buflets, windows, ...)
Time domain used for simple HMI is linked to the low prio HMI task
  TaskID, OSApplication, DisplaySyncEvent -> must be defined accordingly in OIL file
  Trigger="TIME_DOMAIN_EVENT_TRIGGER"
  HMITimeDomain="true“
BUFlet => Link to the RSST surfaces
Display => mapping the display configured in Configuration.xml to the HMI layer
WMApps
  Non-widget painter, example: to clear the whole surface with single color
  Will be used a lot in advanced HMI

## Slide 30: Demo 1 Modelling the drawing task and image assemblies (2)
Windows
  A root window links a BUFlet (place to draw) and TimeDomain (drawing task)
    Each BUFlet must have a root window
  ALL windows defined in CIA folder will be alive all the time (as long as the BUFlet exists)
  Define the window structure according to the tree we have designed
  Assign a painter to draw a content in the window
    Widget / WMApp
  For widget window sub-tree, only the root window needs to be defined explicitly
    Painter: widget tree root
Text
Happy
Visibility
Controller
Scene
#1
Sad
Simple
Gauge
Widget tree
root
Clear
Root
Buflet
(surface)
WMApp
painter
Widget
Painter
(root)

## Slide 31
Application Data Binding

## Slide 32: Sample display requirements (revisit + additional requirement)
85 %
Image change to sad face when value < 20, and smiley when value > 70. In all other case, It’s not showing.
Text displays the numeric value of the bar above.
Center aligned in the middle of the display.
Font : Calibri 30
Color: Red
Green bar shows the current oil level in the range of 0-100.
Bar size: 200 x 40 pixels (centered)
Display size: 240 x 320
Oil level application:
Start at value 0
Increased every second by 5% until 100%
2 widgets
linked to
1 application
API design:
ONCHANGE
Buffered
Getter
Ignore this part for now!

## Slide 33: API Manager
“API Manager“
  - communicates between Applications and Embedded HMI Framework (EPF).
Application
API
Manager
API
Embedded
HMI
Framework
DPOOL
Mirror
API
API
API
<<uses>>
EMBEDDED
TOOLING
Model
XML
Code
Generator
<<defines>>

## Slide 34: Use Case A1 - First XML delivery
Stubs /
templates
Constant
„Start of development“, no API yet implemented
Generate API declarations according to the XML „Performance Specification“
Generate „Prototype“ API Implementations and Configurations (sdh-files)
API
xml
API Generator
Api.c
files
sdh
files
API
1c1.h
API
csv
API
txt
Developer
HMI Performance
Specification
Implement
ODO
Api.c
ODO
sdh
h
files
<<includes>>
<<includes>>
Notes: API.xml entry with parameter is assumed to be setter
If it’s actually a getter API, app developer must change it in sdh

## Slide 35: Use Case A1 - First XML delivery
To implement an API the developer …
  … shifts the generated (ONLY these)
    … API configuration from one of the generated sdh-file to his module
    … API implementation from one of the generated c-files to his module
  Deletes the dummy data definitions (DPOOL stuff) referenced by the generated API
    (only if DPOOL is already defined by existing modeller / application)
In order to see the API function prototype, the data IDs from the API Manager etc.
the module must #include „API_c1.h“
The API prototype must be kept in the generated header files, do not move somewhere else!
Notes: If application is new, we can use the generated DPOOL stubs and adapt the app code accordingly

## Slide 36: Use Case A1 - First XML delivery
The developer has to change a special javadoc comment in order to document
the implementation status of the API
int32 bap_navi_TimeToDestination_TimeInfo_Year ( void ) /* @status Prototype*/
{
/******************************************************************************************
* Funktion gibt den Jahres-Wert zurueck. Der Wert ist nur Verfuegbar, wenn als
* TimeInfoType "ArrivalTime" gewaehlt wurde.
* @response => ONCHANGE
* @return => int32
* @param void
******************************************************************************************/
int32 Value;
APIM_boGetData( APIM_nData_API_bap_navi_TimeToDestination_TimeInfo_Year , &Value, (uint16)sizeof(Value) );
return ( Value );
}
Prototype
Generate
Under Development
Implemented
Obsolete
Notes: Potential issue if comment is not updated properly: duplicates of API as it’s generated again
Only Prototype is a must, other name can be configurable

## Slide 37: Use Case A1 - First XML delivery
int32 bap_navi_TimeToDestination_TimeInfo_Year ( void ) /* @status Development */
{
/******************************************************************************************
* Funktion gibt den Jahres-Wert zurueck. Der Wert ist nur Verfuegbar, wenn als
* TimeInfoType "ArrivalTime" gewaehlt wurde.
* @response => ONCHANGE
* @return => int32
* @param void
******************************************************************************************/
// In order to implement this function, I, the developer changed the comment above
// and will right now start to fill the function with very good code …
return ( 0 );
}
Prototype
Generate
Under Development
Implemented
Obsolete
Notes: For non-prototype, the sdh definition will not be regenerated
Sdh should be modified as per required

## Slide 38: Use Case A1 - First XML delivery
Prototype
Generate
Under Development
Implemented
Obsolete
int32 bap_navi_TimeToDestination_TimeInfo_Year ( void ) /* @status Implemented */
{
/******************************************************************************************
* Funktion gibt den Jahres-Wert zurueck. Der Wert ist nur Verfuegbar, wenn als
* TimeInfoType "ArrivalTime" gewaehlt wurde.
* @response => ONCHANGE
* @return => int32
* @param void
******************************************************************************************/
DPOOL_tstTimeInfo stTimeInfo = {0};
if( APIM_boGetData( APIM_nData_TimeInfo , &stTimeInfo, (uint16)sizeof(stTimeInfo) ) )
{
if( stTimeInfo.biType != TIMEINFO_nType_ArrivalTime ){
stTimeInfo.i32Year = TIMEINFO_nInvalidYear; // return -1 if ArrivalTime is not selected
}
}
return ( stTimeInfo.i32Year );
}

## Slide 39: Use Case A1 - First XML delivery
The code (./src and ./packages) is searched for available API implementations by the used javadoc comment „@status“ behind the closing bracket of the function parameter list
If an implementation is found, the automatic API prototype generation is skipped
For the code parsing the implementation files need to follow a clear naming convention in order to keep the runtime in an acceptable range of some seconds.
    <PACK>_<something>_Api.c

## Slide 40: Use Case A2 – Successive XML deliveries
Templates
For new APIs
Constant
The API’s are now implemented, some might still have “Prototype” status
The tool now only needs to generate new API functions
It must report all deviations between declaration (xml) and definition (implementation)
In below example an existing ODO API implementation deviates to the new xml declaration
API
xml
API Generator
c
files
sdh
files
API
1c1.h
API
csv
API
txt
Developer
Implement
h
files
<<includes>>
ODO
c
ODO
c
ODO
c
ODO
Api.c
FV
API
log
ODO
c
ODO
sdh
communicate

## Slide 41: Use Case A2 – Successive XML deliveries
The tool will notice the deviation and report errors or warnings as shown in the matrix on the first slides.
The tool will generate a csv which shows the implementation status

## Slide 42: Demo 2 Data binding implementation
Define the API at API.xml according to our API design
  Getter, buffered, ONCHANGE
APIGenerator tool
  Generate: .sdh, .c, .h
  Move .sdh and .c to the application module folder
  Implement the API logic (if necessary)
  Update javadoc comments
APIMGenerator tool
  Generate: .sdh
Run Toolchain (important chain: APIGenerator – APIMGenerator – Proseco)
Bind the API with widget
Run Brutus

## Slide 43
Static Scene
Behaviors

## Slide 44: Sample display requirements (revisit + change of requirement)
85 %
Image change to sad face when value < 20, and smiley when value > 70. In all other case, It’s not showing.
Text displays the numeric value of the bar above.
Center aligned in the middle of the display.
Font : Calibri 30
Color: Red
Green bar shows the current oil level in the range of 0-100.
Bar size: 200 x 40 pixels (centered)
Display size: 240 x 320
Oil level application to be controlled by user:
Key RIGHT : increase oil level by 5%
Key LEFT: decrease oil level by 5%
Behavior aspects:
Messaging
(Sub)scene management
Property link
Guard / Condition

## Slide 45: Widget Communication Overview
There are two ways by which external entity can communicate with the widgets, through Messages and through API (data binding). Besides external tasks, messages are also used for internal communications between widgets.
API Widgets can be configured for exchanging data with external entity through APIM and DPOOL
Messages All widgets can receive information or command in form of WCS::Message objects. WCS::Message can carry message ID, type, and memory pool ID, as well as optional receiver ID, and data. The main message receiving interface of the widgets is Handle-Message which consists of these processing:
  Class-specific message processing (Process-Message)
  Instance-specific message processing (Final-Hook)
  Optional special hooks

## Slide 46: Widget Communication Process Message
Widget base class implements generic mechanisms of message processing.
Each widget class may define special behavior or response towards a message, based on message type, ID or data when the message is received, or choose to ignore them.
All derived classes should call their parent class’ message handler method before their specific implementation in order not to miss generic implementations of its base classes.
When derived widget doesn’t define its own ProcessMessage method, the implementation from the base class is used.
It is important for widget to return a correct “message status” after processing the message (in any message processing method / hook). There are 3 possible values:
  BLOCK_MESSAGE Stop the tunneling propagation for this message and start the bubbling process
  PASS_MESSAGE Widget did not do anything, and message should be propagated further.
  CONSUME_MESSAGE Widget reacts on the message, and therefore message should be destroyed.

## Slide 47: Widget Communication Final Hook
A final hook can be configured for each widget instance in the model.
Here one can define some instance specific behavior in reaction to specified messages.
Each widget call’s its final hook method after its class’s message processing method.
Final hooks are generated by Brutus for each widget depending on the model, and thus are not fully under programmer’s control.
Final hooks support both communication using API or messages.

## Slide 48: Widget Communication Special Hooks
Firstly, there are 3 non-virtual methods:
  PreMsgHook_
  MiddleMsgHook_
  PostMsgHook_
These methods implement the widget-generic mechanisms, and are not supposed to be over-written.
Currently, only PreMsgHook_ is in use, while the other two are only for future extensions.
Then, there are 3 virtual methods:
  PreMsgHook
  MiddleMsgHook
  PostMsgHook
These methods are supposed to be over-written (if necessary) with project-specific implementations.
In the base class MiddleMsgHook is responsible for preventing Tunneling messages from entering Final Hook. Therefore, project specific overrides must also take over this role.

## Slide 49: Widget Communication Handle Message
The main method for processing message, HandleMessage, has calls to these new methods before, after and in-between calls to ProcessMessage and Final Hook as below:
  HandleMessage (Message m) { PreMsgHook _ (m) ; PreMsgHook(m) ;
    enProcessMessage (m) ; // class specific method for processing messages
    MiddleMsgHook _ (m) ; MiddleMsgHook(m) ;
    pfGetFinalHookFunc () (this , m) ; // calls final hook of the widget
    PostMsgHook _ (m) ; PostMsgHook(m) ;
  }

## Slide 50: Widget Communication Messaging – Generating Events (1)
Where can you generate events (i.e. post HMI message) from, via the model?
  Widgets (final hooks)
    Property changes (OnChange)
    Transition
  State machines
    OnEntry / OnExit
    Transition
Two key attributes in the model:
  Storage : where the message will be stored temporarily It influences the message delivery order.
  Propagation: how the message will be delivered to the widget (propagation strategy)

## Slide 51: Widget Communication Messaging – Generating Events (2)
There are mainly 4 different set of interfaces supported, depending on the storage where the message is posted.
WAS::Framework::PostMessage
  enqueue messages to the external message queue.
  The memory location used for all these messages is the Memory pool for External messages.
  All message types may be posted to the external message queue.
  Xml example:
  <Event Name="MyWidgetEvent1" Storage="External" Propagation="TopDownBroadcast"/>

## Slide 52: Widget Communication Messaging – Generating Events (3)
WAS::DisplayController::PostMessage
  enqueue messages to the internal message queue of a specific display controller.
  The memory location used for all these messages is the Memory pool for Internal messages associated to the display controller which was used during the call.
  Only a restricted set of messages may be posted here: TREE_BROADCAST_MESSAGE, TREE_TUNNELING_MESSAGE, ADDRESSABLE_MESSAGE, DIRECT_MESSAGE and TREE_BROADCAST_BOTTOM_UP_MESSAGE
  Xml example:
  <Event Name="MyWidgetEvent1" Storage="Internal" Propagation="Addressable" Receiver="V0"/>

## Slide 53: Widget Communication Messaging – Generating Events (4)
WCS::Messenger::PostStackMessage
  enqueue messages to the MessageList.
  The memory location used for all these messages is the EPF memory pool.
  Only a restricted set of messages may be posted here: TREE_BROADCAST_MESSAGE, TREE_BUBBLING_MESSAGE, ADDRESSABLE_MESSAGE, DIRECT_MESSAGE and TREE_BROADCAST_BOTTOM_UP_MESSAGE
  Xml example:
  <Event Name="MyWidgetEvent1" Storage="Stack" Propagation="Addressable" Receiver="V0"/>
Notes: Default storage
Default propagation: bubbling

## Slide 54: Widget Communication Messaging – Generating Events (5)
WCS::Messenger::SendMessage
  send messages directly (they are executed in the same function call i.e. the calling method does not return until the message is not sent and processed).
  All messages generated during this process are local objects on the stack, so they are not created using HMI memory manager and they don’t need to be deleted.
  Only a restricted set of messages may be posted here: TREE_BROADCAST_MESSAGE, ADDRESSABLE_MESSAGE, DIRECT_MESSAGE and TREE_BROADCAST_BOTTOM_UP_MESSAGE
  Xml example:
  <Event Name="MyWidgetEvent1" Storage="Direct" Propagation="Addressable" Receiver="V0"/>

## Slide 55: Widget Communication Messaging – Direct Message Registration
Direct message is a message which sent only to registered receivers. The list of receivers must be specified in the model. Affected xml: Configuration.xml : <Display> : <DirectMessage>
To-do: - Define List of Direct Messages per widget instance / class - Direct Message can be an integer, enum, Virtual Key => During runtime: These Direct messages are sent to these widgets without tree propagation.
Configure Receiver List:
<DirectMessaging>
<Widget Name="V0_B">
<DirectMessage>4</DirectMessage>
</Widget>
<Type Name="Container">
<DirectMessage>12</DirectMessage>
<DirectMessage>23</DirectMessage>
</Type>
</DirectMessaging>

## Slide 56: Scene Management Controller Widget (1)
“Controller Widget” is special type of widget which has a role to manage the sub-tree below it
Each controller widget has a state machine attached to it, to specify all possible sub tree constellation / state
Multiple controller widgets may exist in one widget tree
There are 3 types of Controller Widget in WFC:
  SceneController
  VisibilityController
  TransitionController
Scene Manager 1
Tree Builder
Scene Controller
VisibilityController
Scene Manager 2
Scene Manager 3
TransitionController
Scene Controller

## Slide 57: Scene Management Controller Widget (2)
SceneController applies Lifecycle Control:
  Not all its children are alive at the same time
  The lifetime of children is specified by the state
  When the state changes, it instructs Tree Builder to build / destroy its children as per need
  It’s memory efficient, but may take more runtime during the state change
VisibilityController applies Visibility Control:
  All children all alive at the same time
  Visibility of children is specified by the state
  When the state changes, it changes the visibility of its children as per need
  It needs more memory, but has very fast reaction and able to react on messages
TransitionController is a special type of SceneController
  It allows both old and new tree alive until an explicit “destroy” is requested for the old tree
  It is taking more memory than the usual SceneController
  Usecase: to support transition animation
Notes: Influence on messages received
What happened with common widget?

## Slide 58: Scene Management State Machines
There are 2 kinds of state machine provided by the framework:
  Classical SM (flat)
  Hierarchical SM (with sub-states)
Within one widget tree, multiple state machines can be applied
ARTEMMIS State-Machine supports
  States
  Transitions [Events, Guards, Actions, TargetState]
  OnEntry / OnExit [Events, Guards, Actions]
  History (shallow / deep) – only for Hierarchical SM
A Transition always will be triggered by a message, which leads to a state change or which stays in the current state (self-transition)
An action (as a result of a transition) can be a method invocation, an API update or the generation of new messages
S1: Play
S2: Settings
S3: Help
S11: Play
S12: Setting
S0: Top State
S1: Radio
S2:
Help
classic
state machine
Hierarchical
state machine

## Slide 59: Special Modelling Topic Guards
A guard works like a filter. The evaluation of the guard is performed to decide which action to take or whether the action is to be taken. A guard is just a simple C++ expression which in the end will evaluate to a Boolean value.
There are 2 ways to represent guards:
  XML tag with operator => supports unary, binary, ternary operators
  Example: for a guard if (2!= TestAPI())
  <Guard>
  <BinaryOperator Operator="!=">
  <Term>
  <Constant>2</Constant>
  </Term>
  <Term>
  <API Name="TestAPI">
  </Term>
  </BinaryOperator>
  </Guard>
  Condition string => more details at HMI XML language, or the schema
  Example: for a guard if (2!= TestAPI())
  <Guard Condition="2!=.API{TestAPI}()"/>
Notes: Add the context where guard is placed

## Slide 60: Special Modelling Topic Guards - example
If(WDA.GetOilLevel() < 20)
If(WDA.GetOilLevel() > 70)

## Slide 61: Special Modelling Topic Property Links
A property link is a reference to a property of a widget instance
Property links can be used
  for property values
  <Property Name="Visible"> <PropLink WidgetName=“MyWidget" PropertyName="Visible" /> </Property>
  in guard conditions
  <Term> <PropLink WidgetName=“MyController" PropertyName=“CurrState" /> </Term>

## Slide 62: Demo 3 Sample display requirements (revisit + change of requirement)
85 %
Image change to sad face when value < 20, and smiley when value > 70. In all other case, It’s not showing.
Text displays the numeric value of the bar above.
Center aligned in the middle of the display.
Font : Calibri 30
Color: Red
Green bar shows the current oil level in the range of 0-100.
Bar size: 200 x 40 pixels (centered)
Display size: 240 x 320
Oil level application to be controlled by user:
Key RIGHT : increase oil level by 5%
Key LEFT: decrease oil level by 5%
API design:
ONCHANGE
Buffered
Setter
Widget tree transition:
Event for SM depends
on oil level value.
3 states identified.
Alternative:
Use proplink

## Slide 63: Demo 3 Messaging, SM, DataBinding, Guards, PropLink
Implement enProcessMessage of SimpleGauge:
  If msg ID = VK_RIGHT_RELEASE , CurValue += 5
  If msg ID = VK_LEFT_RELEASE , CurValue -= 5
  Take care of max and min value
Implement API setter linked to CurValue property
Complete the state machine definition
  3 states represents sad, none, happy
  Possible transition between these states
Implement widget tree transition with guards
  If CurValue < 20, send event to change from normal to sad
  If 20 <= CurValue <= 70, send event to change from sad to normal
  If CurValue > 70, send event to change from normal to happy
PropLink between CurValue of SimpleGauge and text widget value

## Slide 64
Thank you for your attention!

## Slide 65
HMI XML Language

## Slide 66: Widget Configuration Widget type descriptions
Definition of all available Widget types (base classes) within a project:
  The widget types (base classes) are given by the framework and are available for a project
  Type: class name
  Namespace: HMI::WFC (should be always this namespace, but new derived widget may use different namespace)
  Declaration file: needed for the generated builder
  SizeOf: object size (information needed for WMMS to calculate the static memory needs. This information is generated by SizeOfGenerator)
   The Widget Type-Description may be extended by project as necessary
<?xml version="1.0" encoding="UTF-8"?>
<Types xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:noNamespaceSchemaLocation="..\XSD\GenericTypeDefinition.xsd">
<WindowType Type="Window" Namespace="HMI::CIA" DeclarationFile="CIA_Window.hpp" SizeOf="40">
<Properties>
<Property Name="PosX" Type="int16" Init="0" EquivalentWidgePropertyName="PosX" />
<Property Name="PosY" Type="int16" Init="0" EquivalentWidgePropertyName="PosY" />
<Property Name="Width" Type="uint16" Init="800" EquivalentWidgePropertyName="Width" />
<Property Name="Height" Type="uint16" Init="480" EquivalentWidgePropertyName="Height" />
<Property Name="Transparent" Type="bool" Init="true" EquivalentWidgePropertyName="Transparency" />
</Properties>
</WindowType>
</Types>

## Slide 67: Widget Configuration Visual Trees
Tip: Use FileLinks to keep the individual XML files small and manageable
<FileLink Name=“…”/>
  Name : Filename of the linked file. Its contents will be treated as if it were expanded into this element’s parent
Defining a Widget instance / visual tree
<Widget Type=“…” Name=“…”>
<Properties>…</Properties>
<Content>…</Content>
<Transitions>…</Transitions>
  Type : The class of the widget (must be declared in TD)
  Name : A unique ID for the widget / visual tree
  Properties : A list of Property values for the widget (only needed if different from default)
  Content (optional) : A list of child Widgets / sub-trees
  Transitions (optional) : A list of Transitions (per-instance behavior)

## Slide 68: CIA Configuration WMapp type descriptions
Definition of all available WMapp types (classes) within a project:
  Type: class name
  Namespace: HMI::CIA (should be always this namespace)
  Declaration file: needed for the generated builder
  SizeOf: object size (information needed for WMMS to calculate the static memory needs. This information is generated by SizeOfGenerator)
   WMapp Type-Descriptions must be extended project specific
<?xml version="1.0" encoding="UTF-8"?>
<Types xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:noNamespaceSchemaLocation="..\XSD\GenericTypeDefinition.xsd">
<WmAppType Type="WMappBlitSurface" Namespace="HMI::CIA" DeclarationFile="CIA_WMappBlitSurface.hpp" SizeOf="20">
<Properties>
<Property Name="ComposeMode" Type="string" Init="GBT_nCompose_Overwrite"/>
<Property Name="ROP" Type="string" Init="GBT_nROP2_Src"/>
<Property Name="SrcMapOpt" Type="string" Init="GBT_nMapOpt_Auto"/>
<Property Name="DstMapOpt" Type="string" Init="GBT_nMapOpt_Auto"/>
<Property Name="ConstAlpha" Type="string" Init="0xff"/>
</Properties>
<Constructor StringOfParameters="(ID)"/>
</WmAppType>
</Types>
Notes: Here we may need to use „Syntax Highlighting“ for a better readability
NOTE: SizeOf is generated by the SizeOfGenerator. Do not provide this information manually

## Slide 69: CIA Configuration Window type descriptions
Definition of all available Window types (classes) of the CIA – Framework
  The window types (classes) are given by the framework
  All available types are available for a project
  Window types are only for the usage at the assembly configuration (CIA.xml)
   The Window Type-Description must not be changed!
<?xml version="1.0" encoding="UTF-8"?>
<Types xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:noNamespaceSchemaLocation="..\XSD\GenericTypeDefinition.xsd">
<WindowType Type="Window" Namespace="HMI::CIA" DeclarationFile="CIA_Window.hpp" SizeOf="40">
<Properties>
<Property Name="PosX" Type="int16" Init="0" EquivalentWidgePropertyName="PosX" />
<Property Name="PosY" Type="int16" Init="0" EquivalentWidgePropertyName="PosY" />
<Property Name="Width" Type="uint16" Init="800" EquivalentWidgePropertyName="Width" />
<Property Name="Height" Type="uint16" Init="480" EquivalentWidgePropertyName="Height" />
<Property Name="Transparent" Type="bool" Init="true" EquivalentWidgePropertyName="Transparency" />
</Properties>
</WindowType>
</Types>

## Slide 70: CIA Configuration CIA project configuration
<CIA xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"
xmlns:xsd="http://www.w3.org/2001/XMLSchema" xsi:noNamespaceSchemaLocation=".\XSD\CIA.xsd">
<Display Name=“CIADemo” TimeDomain=“MainCIA”>
<Buflets ClassName2D=“…” ClassName3D=“…”>… </Buflets>
<TimeDomains ClassName=“…”>… </TimeDomains>
<WmApps>… </WmApps>
<Windows>… </Windows>
</Display>
</CIA>
The CIA configuration contains the whole assembly configuration:
  Configuration of Displays (corresponds to the EPF displays)
  Configuration of BUFlets
  Configuration of TimeDomains
  Configuration of WMapps (definition, overwriting the default parameter given by the Type-Descriptor)
  Configuration of the Window – Tree (assemblies)
    Here all objects are combined/linked together
Notes: Display corrensponds to an EPF Display - Controller

## Slide 71: CIA Configuration BUFlet‘s
<Buflets ClassName2D=“HMI::CIA::BUFlet2D” ClassName3D=“HMI::CIA::BUFlet3D”>
…
<Buflet Name="CIATestAppBuflet3"
Surface="RSST_nSrfcDescLayer0"
PosX=“10“
PosY=“100“
CopyBack=“true”/>
…
</Buflets>
BUFlet configuration:
  Surface : RSST surface desriptor ID
  PosX / Y : only needed in case of a HW-Layer and the position should be not (0 / 0)
  CopyBack : If true, copyback is performed before paint broadcast (only needed for DR Windows)
  Is3D : If true, a BUFlet3D (EGL-based) surface is created instead of the normal 2D (GRLC) surface
  DoFlip : If false, the client is responsible for actually flipping the surface (GRLC_vSurfaceFlip). Otherwise, CIA will do the flip.
  SetVisibility : If false, the client is responsibile for setting the surface visibility in GRLC (GRLC_vSurfaceSetVisibility). Otherwise it is done by CIA after the first flip.
  Priority : BUFlets with higher priority are painted before BUFlets with lower priority (@same TD)
  MaxNumberOfDirtyRects : Used to calculate RAM usage for DirtyRects per for the BUFlet
Notes: Is3D
- Only one buflet is allowed to be 3D for now

## Slide 72: CIA Configuration BUFlet‘s (cont‘d)
<Buflets ClassName2D=“HMI::CIA::BUFlet2D” …>
…
<Buflet …>
<Widget Name=“CIADemo” />
</Buflet>
…
</Buflets>
BUFlet configuration:
  Widget (optional) : If present, the widget window with the specified ID shall be attached to this BUFlet, instead of the HMI tree.
  Type (optional): If the widget being attached is the root HMI widget, this field is not required. Otherwise (e.g., widget is a root of a sub-tree), it must be set to ProxyWindow.
Notes: Widget is not allowed in future.
Widget window of widget that are attached to a BUFlet are CIA windows in future.
This is done to allow the configuration of z-Position.

## Slide 73: CIA Configuration TimeDomains
<TimeDomains ClassName=“HMI::CIA::TimeDomain”>
…
<TimeDomain Name="CIA_enTimeDomainID0"
Trigger="TIME_DOMAIN_VSYNC1_TRIGGER"
Divider=“2“
Semaphore="SEMA_CIA__TD1"
TaskID=“CIA_TDCyclic_1”
OSApplication=“OsApp2”
Context2D=“RSST_nGRLC_CONTEXT1”>
…
</TimeDomains>
TimeDomain configuration
  Trigger: event driven, VSync1
  Divider: in case of VSync1 the divider to control the execution cycle
  Semaphore: Semaphore for time domain and assembler, cross time domain operations (has to be configured at the OS)
  TaskID: The OS task ID used for this time domain
  OsApplication: The OS application name for this time domain
  Context2D: The GRLC context ID used for (2D) painting
  Context3D (optional): The EGL context ID used for (3D) painting.
Notes: Context3D
- Only one TD is allowed to have 3D context for now (just set value to 0)

## Slide 74: CIA Configuration TimeDomains (cont‘d)
<TimeDomains ClassName=“HMI::CIA::TimeDomain”>
…
<TimeDomain Name="CIA_enTimeDomainID0“ …>
<Create SendEvent=“CIA_CreateContextTD1” ProcessingFunction=“CIA_TimeDomain1_Execute” Priority=“1” />
<Process SendEvent=“CIA_ExecuteTD1” ProcessingFunction=“CIA_TimeDomain1_Execute” Priority=“2”/>
<Destroy SendEvent=“CIA_DestroyContextTD1” ProcessingFunction=“CIA_TimeDomain1_Execute” Priority=“3”/>
</TimeDomain>
…
</TimeDomains>
TimeDomain configuration
  Create/Process/Destroy : Elements which describe to CIA how to create,
  process (execute), and destroy the context(s) for the TimeDomain
    SendEvent : The EVHD send event ID to trigger the create/process/destroy
    ProcessingFunction : The EVHD handler that will do the actual create/process/destroy at the right task context. The template for this handler is in the CIA ca file.
    Priority : The EVHD priority for SendEvent
Notes: Brutus generates a Proseco .sdh file accordingly.
(WRS_CIA_gen.sdh)

## Slide 75: CIA Configuration WMapps
<WmApps>
…
<WmApp Name="BlitSwitchViewAnimWMapp" ClassName="WMappBlitSurface" Source="SwitchViewAnim">
<Properties>
<Property Name="ComposeMode" Value="GBT_nCompose_BlendSrcOver"/>
</Properties>
</WmApp>
…
</WmApps>
WMapp configuration:
  Define here all needed WMapps
  Overwrite the default properties of the type description if needed
  Give them an instance name
  ClassName is required for RAM calculation
  Source is optional and is the name of the BUFlet to read from.
  Widget is now obsolete and was used to link ProxyWindows
  ConsiderDependency is true by default. If false the BUFlet, that reads from this surface will not be requested when this assembly is built.

## Slide 76: CIA Configuration Windows
<Windows>
…
<Window Name="HMIWindow" ClassName="Window" >
<Properties>
<Buflet>WidgetTree</Buflet>
<TimeDomain>CIA_enTimeDomainHMI</TimeDomain>
</Properties>
<Children>
<Window Name="ClearHMIWindow" ClassName="Window">
<Properties>
<Painter>CIA_enWMappHMI2</Painter>
</Properties>
</Window>
</Children>
</Window>
…
</Windows>
The Window configuration reflects the designed assembly for a project
  Here all configured objects are linked/configured together
  A window can have all defined properties and in addition <TimeDomains> and <Buflets>
  Here you define the z-Pos and the parent – child relation
  Independent trees are connected via the WMapps and the configured Src-Surface

## Slide 77: State Machines (1)
Defining a new StateMachine
  <StateMachine Name=“…” >
    Name : A unique ID for the state machine
Defining a new State inside a StateMachine or inside another State
  <State Name=“…” VisualElementName=“…”>
  <OnEntry>…</OnEntry>
  <OnExit>…</OnExit>
  <Substates>…</Substates>
  Name : A unique ID for the state
  VisualElementName : The associated visual tree ID (widget ID) for this state
    Note: If more than one visual element, use instead <VisualElements>
  OnEntry/OnExit (optional) : A list of Guards, Actions, and/or Events to check and execute/emit once the state is entered or exited
  Substates (optional) : A list of substates for this state

## Slide 78: State Machines (2)
Defining Transition(s) inside a State
  <Transitions>
  <Transition>
  <Trigger Name=“…”/>
  <Guard Condition=“…” />
  <TargetState>…</TargetState>
  <Actions>…</Actions>
  <Events>…</Events>
    Trigger.Name : The event ID that can trigger this Transition
    Guard (optional) : The specified condition that must pass before this transition is alloweds
    TargetState: The ID of the next State to transition to
    Actions (optional): A list of Actions to execute if this transition occurs
    Events (optional): A list of Events to generate if this transition occurs

## Slide 79: Data Binding (1) – Defining the APIs
API Definitions (API.xml)
  <API UpdateType=“…” ReturnType=“…” Name=“…” HMIApi=“true|false” Description=“…”>
  <Parameter Name=“…” Type=“…” Description=“…” />
  UpdateType : (Unused by Brutus – used only by APIM generator)
  ReturnType : The return value of the API function (void if none)
  Name : The name of the API function (C or C++)
  HMIApi : true if this API is only relevant for HMI Subsystem (no APIM generation will be done for this API)
  Description (optional) : Textual description of the API function
  Parameter (optional) : Only specify if the API needs parameters
    Name : The name of the parameter
    Type : The C/C++ type of the parameter
    Description (optional) : Textual description of the parameter

## Slide 80: Data Binding (2) – Using the APIs
Binding to Widget Properties
  <Property Name=“…”>
  <API Name=“…”/>
  Property.Name : The name of the property to be bound to an API
  API.Name : The name of the API to bound the property to. Must match the type of the Property!
Actions/Guards on a StateMachine Trigger/OnEntry/OnExit
Actions/Guards on a custom Widget Transition

## Slide 81: Guards – Using Condition Strings (1)
The complete guard can be expressed as a “guard string”. Inside this string we support:
1. Support for constants
1.1 Booleans: true and false example: <Guard Condition="3==4"/>
1.2 Integer values: things like 3
1.3 String values: "abcd"
2. Enumerations: .ENUM{EnumerationName}
3. Virtual Keys: .VK{VirtualKeyName} example: <Guard Condition=“.VK{MYVKey}==4"/>
4. RSST IDs
4.1 Text: .TEXT{TextName}
4.2 Bitmaps: .PIX{BitmapName}
4.3 Fonts: .FNT{FontName}
4.4 Widgets: .WIDGET{WidgetName}
4.5 States: .STATE{StatemachineName ; StateName}
5. API invocations:
5.1 API Invocations without parameters: .API{ApiName} ()
5.2 API Invocations with parameters: .API{ApiName} (first , second , third)

## Slide 82: Guards – Using Condition Strings (2)
6. Macros
7. Dependency in Widget Properties (.DEPENDENCY{...} )
Example:
<Property Name="PosX" Dependency="Country: England , Italy ; Language: French”
can also be expressed as:
<Property Name="PosX“ >
<Guard Condition=".DEPENDENCY{Country: England , Italy ; Language: French}"

## Slide 83: Guards – Blocks/if-else
In guard expressions, blocks comparable with C blocks can be defined
Example: <Property Name="PosX"> <Guard Condition="x &gt 3" /> <!-- if (x > 3) --> <Block> <!-- { --> <Guard Condition="y &gt 4" /> <!-- if (y > 4) --> <Constant>1</Constant> <!-- SetPropertyValue(1) --> <Constant>2</Constant> <!-- else SetPropertyValue(2) --> </Block> <!-- } --> <Guard Condition="x &lt 2" /> <!-- else if (x < 2) --> <Block> <!-- { --> <Guard Condition="y &gt 5" /> <!-- if (y > 5) --> <Block> <!-- { --> <Guard Condition="z &gt 6" /> <!-- if (z > 6) --> <Constant>3</Constant> <!-- SetPropertyValue(3) --> </Block> <!-- } --> </Block> <!-- } --> <Constant>4</Constant> <!-- else SetPropertyValue(4) --> </Property>

## Slide 84: Guards – Switch Case
Switch case constructs can be used at all levels of the VDO HMI Language
Example: <Property Name="PosX"> <Block> <Switch Expression="s"> <Case Value="ABC"> <Constant>1</Constant> </Case> <Case Value="CDE"> <Constant>2</Constant> </Case> <Case Value="EFG"> <Constant>3</Constant> </Case> <Default> <Constant>5</Constant> </Case> </Switch> </Block> </Property>

## Slide 85
Backup
Slides

## Slide 86: Design Principles (taken from GS2 UserGuide)
Resources
Contexts
Surfaces
Bitmaps
Texts
Fonts
Lines
Rectangles
CLUTs
Sounds
Render
Engine
All resources will be addressed by IDs
Principles steps for using GS2 System:
Destination Surface and drawing parameter (e.g. drawing color, composition mode et cetera) will be set within the context
For every task you need a separate context. Store context ID returned by function
GRLC API
GRLC_u16GetRenderContext()
GRLC_u16SurfaceCreate()
GOSW_vInit()
GRLC_vSWInit()
GRLC_vHWInit()
GRLC_vDisplayOn()
GRLC_vSetSurfaceID()
GRLC_vPixSetCompMode()
GRLC_vDrawBitmapID
GRLC_vPixSetCompMapOption()
Init GRLC
Get Context
Create Surfaces
Set Destination Surface
(for the current render operation)
- Set Drawing Parameter
- Call Rendering Function
GRLC_vResetSurfaceID
- Reset Destination Surface
DeInit GRLC
GRLC_vReleaseRenderContext
Release Context
GRLC_vDisplayOff()
GRLC_vHWDeInit()
GRLC_vSWDeInit()
GOSW_vDeInit()
Before you can set another destination surface, the current surface has to be released from the context.
Store Surface ID returned by function
Delete Surfaces
GRLC_vSurfaceDelete
CIA
CIA
Painters
Notes: #GRLC_SWInit: initializes RSMG, RSST, ROCH
GRLC_HWInit: initializes GAD

## Slide 87: GRLC "Context" and "Surface“ (taken from GS2 Overview)
Graphical/OSEK
Task
GRLC Context
1
1..n
(Target)
Surface
1
0..1
Srfc-Descriptor
ClipList
1
1
1
1
GRLC Context is standing for the printer engine !!!
Surface is standing for the paper !!!
Relationship detailed in UML:

## Slide 88: Legend
Painter
Widget
Layer
Root
Window
BUFlet
Time
Domain
Context
WMapp
Surface
Widget
Tree
Time
Domain
Display
Cyclic Time Domain
Event-driven Time
Domain
Root Window
Normal Window
Generic Painter
WMapp
Widget
Widget Tree
Offscreen
Surface
Visible
Surface
GRLC
Context
BUFlet
Display

## Slide 89: Typical Configuration (HMI without Animations)
Time
Domain
Display
Context
Root
HMIWnd
Window0
Widget
Tree
BUFlet
Layer
ClearApp

## Slide 90: Advanced APIM Features (refer to spec for more details)
Routing EVHD events to the HMI input queue
  Mapping EVHD to HMI::boSendMessage()
  In case of queue overflow, it’s possible to configure how APIM will react: pass, delay, discard
Cyclic triggering of the HMI subsystem
  Cyclic update of freezebuffer data, update needed in sdh to configure API timer
  Only ONCHANGE is overrideable
Event-driven Triggering of the HMI subsystem
  Update immediately as triggered, even when data is not changed
Repetitive copying of DPOOL data into freeze buffer during locking freeze buffer data
  Trying to update the freezebuffer content with new value if it’s interrupted during copy
  Timeout should be set
Multiple data copying of DPOOL data into freeze buffer in single critical section lock
  Optimize the copy time by clustering freeze buffer updates within 1 critical section lock

## Slide 91
Thank you for your attention!