## Slide 1: HMI Training
05 Animations
Thomas Staebe

## Slide 2: Lecturer
Thomas Staebe
Animation Architect (Ford)

## Slide 3: Topics
Displays, Layers, Surfaces, Buflets
Windows and Painters (Widgets, Animations)
Time domains (Event driven, Cyclic, VSync)
Compositors
Animations (Storyboards, Scenes, Painter Effects)
Interaction between Widgets and Animations
Example: Menu animation

## Slide 4: Surface
A surface is an area in the RAM which contains graphic data e.g. Color Format: RGBA8888 (4 Byte per Pixel)
RGBA means one 1 byte value for red, for green for blue and for alpha
Alpha means transparency, 0 = 0 %, full transparent, you can “see” the content underneath 255 = 100 %, full opaque, you can not see what is underneath
7f 7f 7f ff 7f 7f 7f ff 7f 7f 7f ff ... 7f 7f 7f ff
7f 7f 7f ff 7f 7f 7f ff 7f 7f 7f ff ... 7f 7f 7f ff
...
7f 7f 7f ff 7f ff 7f ff 7f 7f 7f ff ... ff 7f 7f ff
7f 7f 7f ff 7f ff 7f ff 7f 7f 7f ff ... ff 7f 7f ff
...
7f 7f 7f ff 7f ff 7f ff ff ff 7f ff ... ff 7f 7f ff
7f 7f 7f ff 7f ff 7f ff ff ff 7f ff ... ff 7f 7f ff
...
7f 7f 7f ff 7f 7f 7f ff ff ff 7f ff ... 7f 7f 7f ff
7f 7f 7f ff 7f 7f 7f ff ff ff 7f ff ... 7f 7f 7f ff
...
7f 7f 7f ff 7f 7f 7f ff 7f 7f 7f ff ... 7f 7f 7f ff
7f 7f 7f ff 7f 7f 7f ff 7f 7f 7f ff ... 7f 7f 7f ff
…
visual representation
numerical representation

## Slide 5: Display, HW-Layer
A HW-layer is a special surface. The data is read by the Video Output device to generate the Video Signal for the display
The Video Output scans the HW-Layer pixel by pixel and calculates the resulting pixel color for the display
The display gets the video data from the Video Output device via Video signal.
Display
Video out
HW-Layer 3
HW-Layer 2
HW-Layer 1
HW-Layer 0

## Slide 6: Windows
Windows divide a surface into smaller areas
Windows can cover each other completely or partly
A window tree manager determines which window needs to be painted e.g. a window which is completely covered by another non-transparent window does not need to be painted
Windows do not have their own memory, they use the memory of the associated surface!
Window
Surface

## Slide 7: Painter
Every window has its own painter
Painters can be used in widgets or in animations
The painter is responsible for rendering the content of a window
Painters are triggered by the window tree manager via invalidation of the associated windows
Rendering is done by the graphic subsystem
A painter can only paint inside its window. Any painting outside of the assigned window is clipped
Widget Tree
Widget
Widget
Widget
Painter
Windows
Surface
Painters

## Slide 8: Window Manager Application (Painter)
A (animation) painter is used to copy / blit the content of one surface to another
They run with a defined cycle time
Their properties can be influenced by animations
They are used for display information which has to be provided very fast
Properties: - Source Pos/Size - Destination Pos/Size - Blend Modes - Color / Alpha Factors
Modes: - Blit Surface - Draw Bitmap (from RSST) - change Layer Properties
There can be special Painters for special purposes e.g. pointers in a gauge, telltales, warping

## Slide 9: Buflet
A Buflet is a abstraction of a surface inside of ARTEMMIS
It manages the buffers of a surface
It handles the flip operation
It hides the buffer management to the windows
It optimizes the drawing operations on surface level
Surface
Buflet

## Slide 10: Buflet Sections
A Buflet has at least one Buflet section, which covers the whole Buflet (called “main section”)
A window tree has to be attached to a Buflet section
A Buflet can be divided into several parts by Buflet sections
Buflet sections are not allowed to overlap
It is less “expensive” to use Buflet Sections than to use multiple Buflets
Surface
Buflet
Buflet Section
Surface

## Slide 11: Time Domains
Time Domains can be thought as OS tasks
Time Domains can be executed event driven or cyclic
A HMI Time Domain runs event driven: - That means it is executed only if there is something to do - The message and data processing of the widgets is done here - The rendering of the widgets is done here - It has a low priority and therefore runs if nothing else is to do - The rendering of the widget content can take a lot of time (especially when texts are rendered) -> Reaction time is not predictable!
An animation Time Domain runs cyclically, with a defined frequency: - It is triggered by the VSync interrupt - only fast graphic operations are allowed (not text rendering!)

## Slide 12: Synchronization
Problem: - Widgets are rendering in the HMI Time Domain (event driven) - Animations may use the content rendered by the widgets in the cyclic animation Time Domain - The animations do not know when the widgets are finished with rendering - The widgets do not know when the Animations are started
Solution: - Double Buffer - Flip Lock - Consistency Points

## Slide 13: Double Buffer
A double buffered surface consists of two buffers: - one for writing, called “Back Buffer” - one for reading, called “Front Buffer”
When writing to the “Back Buffer” has finished the surface is flipped synchronous to the VSync of the display
The reader always gets a completely rendered image
Flipping the buffers means exchange of pointers (very fast)
Buffer 1
Painter
Buffer 2
Front Buffer
Back Buffer
Display
Front Buffer
Back Buffer
Buffer 2
Painter
Buffer 1
Front Buffer
Back Buffer
Display
Buffer 1
Buffer 2
VSync

## Slide 14: Consistency Point
The widgets start with message and data processing
Then they will do their rendering
When the rendering is done a Consistency Point is reached
Now the widgets have to wait until the animations have drawn their first frame (first frame painted)
During the next VSync the animations will be started which were requested during the message processing of the widgets
 | Vsync |  |  |  |  | V |  |  |  | V |  |  |  | V |  |  |  | V |  |  |  | V |  |  |  | V |  |  |  | V |  |  |  | V |  |  |  | V | 
 | Painter |  |  |  |  |  |  |  |  | A |  |  |  |  |  |  |  | A |  |  |  |  |  |  |  | A |  |  |  | A |  |  |  | A |  |  |  | A | 
 | Flip |  |  |  |  |  |  |  |  | F |  |  |  |  |  |  |  | F |  |  |  |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  | F | 
 | Widgets |  |  |  | M |  | P |  | C |  |  | M |  | P |  | C |  |  |  |  | M |  | P |  | C |  | M |  |  |  | M |  |  |  | P |  | C |  | 
 | Legende: |  |  |  |  |  |  |  |  |  |  |  |  |  | F | Flip of Widget Surface |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | V | VSync |  |  |  |  |  |  |  |  |  |  |  |  | M | Message processing by Widgets |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Animation is wating for start |  |  |  |  |  |  |  |  |  |  |  |  | P | Painting |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | A | Animation/Painter working |  |  |  |  |  |  |  |  |  |  |  |  | C | Consistency point |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 15: Flip / Flip Lock
If the rendering is done a Flip request is set
During a VSync the Flip is executed so a Surface can be read by the Video Output without having inconsistent content
If a animation painter needs a lot of time for the reading of Surface data it can set a Flip Lock. That prevents the surface from being flipped during read access (e.g. Warping needs about 25 ms for reading)
 | Vsync |  |  |  |  | V |  |  |  | V |  |  |  | V |  |  |  | V |  |  |  | V |  |  |  | V |  |  |  | V |  |  |  | V | 
 | Painter |  |  |  |  |  |  |  |  | A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | A |  |  |  |  |  |  |  |  | 
 | Flip Lock |  |  |  |  |  |  |  |  | L |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | L |  |  |  |  |  |  |  |  | 
 | Flip |  |  |  |  |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Widgets |  |  |  | M |  | P |  | C |  |  | M |  | P |  | C |  |  |  |  |  |  |  | M |  | P |  | C |  |  |  |  |  |  | 
 | Legende: |  |  |  |  |  |  |  |  |  |  |  |  |  | F | Flip of Widget Surface |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | V | VSync |  |  |  |  |  |  |  |  |  |  |  |  | M | Message processing by Widgets |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | L | Animation is wating for start |  |  |  |  |  |  |  |  |  |  |  |  | P | Painting of |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | A | Animation/Painter working |  |  |  |  |  |  |  |  |  |  |  |  | C | Consistency point |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 16: Composition
New in ARTEMMIS 4
An additional step was introduced which takes place after the Painting of the widgets and animations: -> Composition
The Composition puts all parts of the final image together on a HW-Layer
A compositor runs in a cyclic task as the animations
Widgets
Widgets
Animation
Compositor
HW-Layer
Off-Screen Surface
Off-Screen Surface
Off-Screen Surface
Animation
Off-Screen Surface

## Slide 17: Compositor
Off-Screen Surface
Off-Screen Surface
The configuration of a Compositor contains a List of Virtual Layers
A Virtual Layers contains a Buflet Section as input and properties that influence the composition (like transparency, src/dest areas, etc.)
A Blend Operation can be configured individually for every Virtual Layer
Off-Screen Surface
Compositor
HW-Layer
Virtual Layer 1
Virtual Layer 2
Virtual Layer 3
Virtual Layer 4
Virtual Layer 5
Section 2
Section 1
Section 1
Section 1
Buflet Sections
Destination Buflet

## Slide 18: Animation
Animation2
Animation1
op
op
op
S
op
op
S
W
W
W
Hardware Layer
Offscreen Surface
Menu
Menu
Animation Preparation Phase
Animation Real-time Phase
op
Rotate
Scale
Copy
Alpha
Move
op
Paint
op
Paint
op
Paint
Copy
Offscreen Surface
Visible Surface
Rotation
Scaling
Movement
Copying

## Slide 19: Animation Concept
Widgets render their content into Off-Screen Surfaces. (Text, Menu Lists, whole Screens, …)
The widgets trigger the animations
The animations painters use the content drawn by the widgets as input for the animations
Animation change the animation painter Properties and make the associated windows invalid to trigger a redraw
Window tree manager calls the painters for the invalid windows
The animation painters draw their content with the changed properties into the windows on a HW-Layer or OffScreen surface

## Slide 20: Animation Concept
Interactions between widgets, animations, painter, windows, window tree manager
Window tree manager
Widget Tree
Widget
Widget
Widget
Animation Painter
Animation
trigger
VSync
Time
Tick
change
properties
paint
invalidate
Window
Windows
Surface
paint
trigger
painting
1
2
3
4
5
6

## Slide 21: Structure of Animations
Storyboard - Can be triggered and stopped by widgets - A storyboard contains scenes - The start time of every scene can be specified - The start type can be configured
Scene - Contains parameters
Parameter - A parameter changes an animation painter property - It contains start and end value - It defines the duration - It defines the algorithm (Easing)

## Slide 22: Structure of Animations
Storyboard 1
  Scene 1 (Mode, Start Time)
    Parameter 1 (Painter, Property, Easing, Start/Stop Value, Duration)
    Parameter 2 (Painter, Property, Easing, Start/Stop Value, Duration)
    Parameter 4 (Painter, Property, Easing, Start/Stop Value, Duration)
  Scene 2 (Mode, Start Time)
    Parameter 1 (Painter, Property, Easing, Start/Stop Value, Duration)
Storyboard 2
  Scene 3 (Mode, Start Time)
    Parameter 3 (Painter, Property, Easing, Start/Stop Value, Duration)

## Slide 23: Easing
The algorithms for calculation the values for the painter properties are called Easings

## Slide 24: Example Animation: “Menu List”
Animation effects:
  Slide in/out of the whole Menu
  Cursor Move up/down
  Menu Scrolling up/down
  Entry Selection effect

## Slide 25: Start Types of a Scene
Frame Based the start time of a scene is configured in the Storyboard (e.g. Welcome)
On Demand The Scene can be starte by a Widget during the Storyboard ia running (e.g. Move, Action)
OnFinish The Scene is started when the Storyboard is stopped explicitly by Widget (e.g. Goodbye)
Endless If a Scene is marked as endless the Storyboard will not be destroyed until it is stopped by a Widged. (e.g. Idle)
Welcome
Goodbye
Idle
Move
(Left,Right,Up,Down)
Action
Frame-based
OnFinish
OnDemand
OnDemand
Endless
(NumberOfFrames=0)

## Slide 26: Interruptibility Matrix
Interaction between a new Storyboard which should be started and already running Storyboards can be configured in a Matrix:
Run: The new Storyboard will be started in parallel to a running Storyboard
Wait: The new Storyboard has to wait until a running Storyboard finishes.
Cancel: The new Storyboard will be dropped if a running Storyboard exits
Stop: The new Storyboard will be started, and a already running will be stopped

## Slide 27: Summary
Surfaces: OffScreen surface, HW-Layer
Buflets: wrapper for Surfaces in ARTEMMIS
Windows: areas on a Surface, assigned to painters
Painter: draws the content of a window
Compositor: composes the final image
Time Domain: event driven, cyclic
Synchronization: Double Buffer, Consistency Point, Flip Lock, First Frame painted
Animation: changes Painter properties
Storyboards: started (stopped) by Widgets
Scenes: Frame Based, OnDemand, OnFinish, Endless
Parameter: influences Painter properties
Interruptibility Matrix: interaction between Storyboards