## Slide 1: HMI Training
09 Additional exercises
Felix Opatz

## Slide 2: Referenten
Felix Opatz
HMI System Designer (PF3 NG)

## Slide 3: Topics
Description of base system
Additional exercises
  A01: Activation/deactivation of training screens
  ...
Resources

## Slide 4: Description of base system
Bases system is
  a recent PF3 NG software frame, e.g. 213 IC HL
  containing the integrated HTPKG package
Each additional exercise requires all previous exercises to be finished successfully
Generally it is easier to stay within the same base system, but don't be too scared to port your package to a different system!
HTPKG as defined by HMI_08_Exercises.pptx
Additional exercise A01
Additional exercise A02
Progress

## Slide 5: A01: Activation/deactivation of training screens (1)
In the original HMI training exercise the Scene Controller placed its DAM-p request upon creation
Now activation/deactivation should be controlled by a CAN signal that can be changed at runtime
For simplicity we will use an indicator lamp that is handled by SOM, so we already have a DPOOL item we can access
  CAN signal: ABS_IndLmp_On_Rq
  SOM channel: SOM_nenLampABS
  DPOOL item: SOM_au8LampState
Byte 0 |  |  |  |  |  |  |  |  | Byte 1 |  |  |  |  |  |  |  |  | Byte 2 |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Example: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | SOM channel = 12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Byte= 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Bit = 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 6: A01: Activation/deactivation of training screens (2)
TODOs
  Create an API function that checks for the lamp state
    Should be sufficiently generic to be changed to a different lamp easily (e.g. one single place to insert SOM channel ID)
  Extend the Scene Controller's state machine to
    Trigger on the Update Data Binding message
    Set the DAM-p request when the lamp is turned on
    Clear the DAM-p request when the lamp is turned off
Hints
  Consider using a hierarchical state machine
  When you think you are done with the API function, try using a lamp whose state is not located in the first byte of SOM_au8LampState (e.g. HUD ESP lamp or indicator left)

## Slide 7: Resources
HMI Training slides
  Intranet, search for "HMI-Schulung"
HMI System Design specification
  Stored in MKS (ask a colleague if you don't have access): #/id/dag_PF3/sw#com/Design/HMISys/~dag_PF3.sw.com.HMISys_IC213GC_HL

## Slide 8: Kontakt
Schleißheimer GmbH
Am Kalkofen 10 D-61206 Wöllstadt Tel.: +49 6034 9148-701 Fax: +49 6034 9148-91 vertrieb@schleissheimer.de
www.schleissheimer.de
www.CanEasy.de
Die anwenderfreundliche Analyse- und Testumgebung sowie Restbussimulation für CAN und LIN – Jetzt testen und Zeit sparen.